## Slide 1: Rostering of air traffic controllers - flexibility in time and space
Goran Pavlović – University of Belgrade / EUROCONTROL*
*The views expressed in this presentation are the author’s own and do not represent a policy or position of EUROCONTROL
Acknowledgements:
Radosav Jovanović & Milan Stanojević – University of Belgrade

## Slide 2: Content
Why scheduling/rostering matters?
Capacity management in ANSPs
Rostering flexibility in time
Rostering flexibility in space
Summary of results

## Slide 3: why rostering matters?
Staffing - major cost component in the total ATM/CNS costs (labour intensive activity)
At the same time one of the main reasons for delay in the network
More and more challenging to recruit, train and retain ATCOs
High heterogeneity in rostering practices applied across ANSPs/ACCs in Europe
Evidences of spare capacity – but when, where?
Source: ATM Cost-Effectiveness (ACE) Benchmarking report 2019
Source: Performance Review Report (PRR) 2019

## Slide 4: Capacity management in ACC
capacity
demand
Cost-efficiency
uncertainty/volatility in time
and space
added in larger chunks
(sectors -> shifts -> ATCOs)
ACC – Area Control Centre
ATCO – Air Traffic Control Officer
In order to accommodate traffic demand, airspace is divided into smaller segments - “sectors” (elementary and/or collapsed), each served by a pair of ATCOs – planner and executive.
?

## Slide 5: Rostering model
Objective function:
(1) To minimize the number of ATCO pairs (i) engaged during one day of operations, represented by a given capacity profile/Sector Opening Scheme.
Constraints:
(2) - link between variables and , i.e. an ATCO pair isv considered engaged (= 1) only if it is assigned to a shift. The number of shifts assigned to an ATCO pair does not exceed 1.
(3) - the minimum number of available ATCO pairs at any time period is greater than the number of open sectors in the same period
(4) and (5) - limitations for decision variables (binary).

## Slide 6: Flexibility in time – case study
to capture different capacity profiles and levels of ATCO rostering flexibility
to assess key relationships, not to build an actual roster for an ACC!
generic (common) assumptions - not to replicate any specific ACC and its local operational and/or social conditions:
  maximum consecutive time at operational position 2 hours
  minimum duration of break away from the position 30 minutes
  maximum shift duration 8 hours
  time for briefings before taking up duty, as well as time needed for handovers at the operational position considered to be relatively short and therefore not taken into account

## Slide 7: Flexibility in time - INPUT
Three capacity profiles with different hourly variability
Different levels of rostering flexibility:
Basic pattern with 3 shifts
6 shifts (3 basic + 3 staggered shifts in increments of 2 hours)
10 shifts (3 basic + 7 staggered shifts in increments of 1 hour)
18 shifts (3 basic + 15 staggered shifts in increments of 30 min)
Chart: ACC 3
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 2 | 2 | 2 | 2
Chart: ACC 2
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 5 | 5 | 6 | 6 | 5 | 5 | 6 | 6 | 6 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 6 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 3 | 3 | 2 | 2 | 1 | 1
Chart: ACC 1
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 8 | 8 | 8 | 8 | 8 | 8 | 9 | 9 | 8 | 8 | 7 | 7 | 6 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 3 | 3 | 2 | 2 | 1 | 1

## Slide 8: Flexibility in time – key takeaways
Number of ATCOs:
increases linearly with sector-hours
savings reduce with the flattening of the demand profile
the increase is generally slower for smoother profiles
up to 20%
Spare ATCO-hours:
largest capacity wastage occurs in low traffic conditions
gradually decreases with more flexible shift designs and flatter demand/capacity profiles
always present - inability to perfectly match supply with demand
More info:
Pavlović, G., Jovanović, R., & Stanojević, M. (2023). Rostering of air traffic controllers–current practices in Europe, key performance trade-offs and future opportunities. Journal of Air Transport Management, 113, 102472.

## Slide 9: Flexibility in space?
Cross-border operations
Capacity-on-demand concept
“Any controller, any airspace”
Ongoing research:
  PJ10 PROSA
  PJ33 FALCO
Source: Airspace Architecture Study (2019)
FINEST project
What are the ACCs that have the greatest potential benefit from cross-border operations, based on their traffic demand/capacity profiles?
Chart: 
base | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 3 | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 3 | 3 | 3 | 3 | 3 | 2 | 2 | 1 | 1
diff | 0 | 0 | 0 | 0 | 0 | -1 | -1 | 0 | 2 | 2 | 2 | -1 | -1 | -1 | -1 | 2 | 2 | 1 | 1 | -1 | 0 | -1 | 0 | 0
ACC 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 4 | 4 | 4 | 3 | 3 | 3 | 3 | 5 | 5 | 4 | 4 | 2 | 2 | 1 | 1 | 1
ACC 2 | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 3 | 2 | 2 | 2 | 4 | 4 | 4 | 4 | 3 | 3 | 3 | 3 | 3 | 2 | 2 | 1 | 1

## Slide 10: Flexibility in space – case study
85 ACCs/sector groups simulated (ECAC area without Azerbaijan & Iceland)
EUROCONTROL NEST (Network Strategic Tool) used to simulate Sector Opening Schemes
4 days of 2018 (Monday & Saturday in Winter & Summer)
3 shift designs with 3, 6 and 12 shifts
Two step approach:
  savings matrix (85 x 85 ≈ 7225 potential pairs)
  savings maximization by optimally matching/pairing ACCs
12 scenarios/runs

## Slide 11
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 12
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 13
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 14
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 15
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 16
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 17
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 18
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 19
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 20
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 21
Optimum ACC pairing – TOP 10
(based on avg. savings across 12 scenarios)

## Slide 22: Summary - Flexibility in time and space
Chart: Summer Saturday - full ECAC
| 3 | 6 | 12
individual rostering | 4170 | 3816 | 3576
optimum ACC pairing | 3962 | 3600 | 3372
"super ATCO" | 3887 | 3540 | 3274
TIME only: -14% (≈600 ATCOs)
SPACE only:
“super ATCO” -7% (≈300 ATCOs)
ACC pairing -5% (≈200 ATCOs)
TIME + SPACE:
“super ATCO” -21% (≈900 ATCOs)
ACC pairing -19% (≈800 ATCOs)

## Slide 23
Thank you for your attention!
Questions/suggestions/remarks?
Contact:
goran.pavlovic@eurocontrol.int