## Slide 1: Network delay optimisation of multiple CASA regulations in fragmented European airspace
Sergio RUIZ (PJ09.3 A-DCB)
14 MAY 2019

## Slide 2: Outline
Introduction and motivation
Optimisation heuristics used (ECASA)
Experimental setup
Simulation results and discussion
Conclusions

## Slide 3: Introduction & motivation

## Slide 4: Interacting regulations and their effect in the total network delay
The problem becomes bigger when congestion grows ( more regulations = more probability of interactions)
Delay x2 in this small example
Performance Scheme is distorted (is it fair for the FMP in R1?)
Delay increases with the interactions between regulations

## Slide 5: Realistic example of complex interactions between regulations
In the example, 95 flights delayed by KEAST28N generated more than 45 h of extra/unnecessary delay in the network
KEAST28N
Delay could be reduced with a net-centric view of the ATFCM processes
The local FMPs declare regulations with no awareness of the impact on other sectors or on the network

## Slide 6: Motivation & research approach
Fragmentation problem: non-smoothed coordination of the local ATFCM processes (ATFCM processes are today done locally with little awareness of the impact on other sectors)
Research question: can the network-centric (de-fragmenting) optimisation of multiple CASA regulations improve the performance of fragmented EU airspace?
Enhanced CASA (ECASA) is under development today at EUROCONTROL to optimise the network delay globally with a net-centric approach
A case-study will be presented in which ECASA is applied in a single FAB in ECAC (ideal Single European Sky). The effect in some delay KPIs will be assessed for FABEC and MUAC sectors to give answers.

## Slide 7: Optimisation heuristic used (ECASA model)

## Slide 8: Enhanced CASA (ECASA)
ECASA principle: apply small amendments to the default CASA sequences to optimise the network performance taking into account the Interacting Regulations problem
ECASA algorithm:
  At each CASA True Revision Process (every 1-5 minutes):
    Run CASA as usual (CASA is the core)
    Identify the flights to be amended (for network optimisation)
    Change the priority for those selected flights
    Run CASA again. Slot changes will be applied by CASA
ECASA
ECASA follows an innovative approach (min change with max benefit)

## Slide 9: Optimisation strategy proposed by ECASA
ECASA makes a better use of the available capacity to reduce the total delay

## Slide 10: CASA simulation results analysis (AIRAC 1708)
The average delay increases with the number of regulations.
More regulations, more delay
More regulations, more capacity inefficiencies (empty slots)
The average number of empty slots also increases (capacity inefficiencies)  it is perhaps the cause of the delay increase

## Slide 11: How ECASA optimises: manual example
Flights can be sorted by optimisation potential
This flight for instance could potentially reduce the delay of 218 flights
HMI used in RNEST

## Slide 12: In this case two regulations are penalised by the selected flight
In this case the flight can optimise the delay in 2 different regulations (175 flights in one + 45 in the other = 218 flights)

## Slide 13: Penalisation of MGY3428M to MGY1228A
Note: approx. ETO position of the flight
If the delay of the flight in 1 is reduced by 24 min in MGY3428M then it will take a free slot in 4-5 instead of the slot in 2-3, thus saving 45 * 2 = 1.5 h delay in MGY1228A

## Slide 14: Penalisation of MGY3428M to EHYR28
If the delay of the flight in 1 is reduced by 24 min in MGY3428M then it will take a free slot in 6-7 instead of the slot in 2-3, thus saving 175 * 1:20 = 4 h delay in MGY1228A
Note: approx. ETO position of the flight

## Slide 15: Experimental setup

## Slide 16: Simulation tool used: R-NEST Airspace simulated: ECAC Airspaces analysed: FABEC & MUAC
Main assumption: 1 single FAB covering ECAC (ideal SES concept)

## Slide 17
ECASA performance will be analysed with these KPIs:
Delay in the network
Impact to AUs
Research methodology
Data from AIRAC 1808 (mid Jul to mid Aug 2018)

## Slide 18: Results and discussion

## Slide 19: The more congestion the more optimisation potential
Optimisation in ECAC: between 18% and 35% (27% avg)

## Slide 20: Average delay per regulation in the period (AIRAC 1808)
-30% minutes of delay
-31% minutes of delay

## Slide 21: Total number of flights delayed in the airspace considered
-1064 flights delayed (-16%)
-221 flights delayed (-19%)

## Slide 22: Number of flights delayed a certain number of minutes (delay distribution)
Typically, delays of less than 15 min can be considered negligible in terms of costs for the AUs
>15 min
<15 min
>15 min
<15 min
-50% flights delayed >15 min
-56% flights delayed >15 min

## Slide 23: Share of flights in the CASA regulation sequences vs ECASA sequences
CASA
ECASA
Less % of flights delayed and less slots forced by external regulations
+ 13 points
-10 points
-3 points
-8 points
+ 15 points
-7 points

## Slide 24: conclusions

## Slide 25: Conclusions
The ATFCM processes are today done through local decisions with little awareness of the impact on the network
A centralised (de-fragmenting) coordination of the ATFCM slots allocation (e.g., through ECASA) could contribute to reconcile the various needs at local and network level
Substantial delay reductions have been achieved in simulations with ECASA (30% less delay in FABEC and MUAC compared to CASA, and 50% less flights delayed more than 15 min)
It is foreseen that a change in the performance scheme might be also necessary to encourage and smooth the operational coordination between ANSPs (& to include the ‘impact of delay’)

## Slide 26: Back-up slides

## Slide 27: Number of regulations in FABEC in busiest period of summer 2018
Days analysed: from 20th July to 15th Aug 2018 (AIRAC 1808)
5152 regulations analysed in total
190 regulations per day in average
110 min, 322 max

## Slide 28: Optimisation strategy implemented in ECASA
F in its ETO position

## Slide 29: Number of regulations and (simulated) delay per day in FABEC

## Slide 30: Definition of tension zones
Tension Zones: periods/positions in the sequence in which flights can take earlier positions (note: typically in TZs there is delay)
Regulation period

## Slide 31: Properties of the interactions on flights: accumulative and commutative
Accumulative: the total net impact on a flight is direct addition of all the impacts received
Commutative: the order of the impacts does not alter the final sequence.
Note: Intermediate states and impacts may evolve differently with the change of order (but does not affect to the final sequence)
Simple example: flights forced in R1 by another MPR
Order 1:
First B, then X
Order 2:
First X, then B

## Slide 32: Penalisations and Protections to TVs due to Regulations (network stability)
1
3
4
1
2
3
4
Throughput of traffic volume B before regulating traffic volume A
Throughput of traffic volume B after regulating traffic volume A
Penalising flights: the delay produced by A pushes flight f1 inside the observed period
Protecting flights: the delay produced by A pushes flight f2 outside the observed period
Common demand is the set of flights that get through at least traffic volumes A and B.
f1
f2
f1
f2
Throughput must be considered in addition to delay  We will optimise capacity usage to minimise delay
ECASA solutions should not de-stabilise the network  TVs should not receive too many additional flights

## Slide 33: Definition of impact to AUs
Cost of delay on 1 flight
Delay
Non-linear cost structure due to :
PAX flow: transit, high yield
passengers, rotations,…
Resource Mgt. (cascade): curfew,
crew constraints, pilots
constraints, maintenance, ...
Impact = large
Impact = 0
Impact = acceptable
Impact = acceptable
Impact = large
Flight on planned or re-planned time
(delay = 0)
Typically, delays of less than 15 min have negligible costs for the AUs

## Slide 34: Strategy 1: Avoid flights entering into Tension Zones (of other regulations)
Slot used
Out of R3
Empty slot
Removing flights from the beginning of large tension zones can save hours of delay in a single regulation

## Slide 35: Strategy 2: overloading slots nearby the existing empty slots
Case 1:
 Better usage of spare capacity (slots) with no negative impact on ATC workload and important reduction of delay
Case 2:
 Idem, but using the empty slots in the middle of the sequences
Empty slot
Used slot (compensating the nearby overload)
Used slot (compensating the nearby overload)

## Slide 36: Strategy 3: systematic overloading of slots
Sometimes the ATCOs may have less workload if the traffic is smoothed by a regulation (less probability of bunching  less complexity and less workload): TBC by ATC experts
This situation could perhaps be improved by adding a second rate parameter under control of the FMP: the overloading rate (e.g.: rate 60/3  1 overload every 20 minutes)
Important delay reductions are expected, while the ATCO’s actual capacity could be better used during periods of congestion