## Slide 1: AFUA Implementation in Lower Airspace Through Modular Flexible Structures
by Ranko Vuica and Željko Savić
Croatia Control Ltd.

## Slide 2: Introduction
COMMISSION REGULATION (EC) No 2150/2005 of 23 December 2005
„Flexible use of airspace is an airspace management concept described by the International Civil Aviation Organization (ICAO) and developed by the European Organization for the Safety of Aviation (Eurocontrol), according to which airspace should not be designated as either purely civil or purely military airspace, but should rather be considered as one continuum in which all users’ requirements have to be accommodated to the maximum extent possible.”
AFUA implementation in Lower Airspace through the Modular Flexible Structures
Project results: „New modular flexible environment in lower airspace supports various activities in airspace, extends new possibilities for airspace use to all kinds of users and at the same time positively influences the awareness and safety of all users.”

## Slide 3: Users’ Perspective
Complexity of lower airspace
  Airspace classes (G, C, D)
  Airfield and aerodrome operations (CTR)
  Non AMC-manageable military areas (P, R, D)
Various types of users
  Military
  Police
  SAR
  Sporting activities (gliding, paragliding, etc.)
  General aviation
  Balloons, free balloons, RPAS/UAS
Various needs
  Permanent airspace (location and height) vs AD-HOC areas
  Huge areas vs small areas
  Adjustable airspace (lateral and vertical boundaries)
  Time of use (seasonal, on weekends, daily, hourly)
Avoidance of the full area establishment process
Abuse of AD-HOC principles
  Continuous renewal of the approval for AD-HOC-created areas (permanent areas)
Requested time of use
  Not realistic (3 months SR – SS)
Uncertainty of operations
  Tactical approval depends on the actual situation
Difficult planning process for other users
  Uncertain real-time status of an area − (active, non-active)
Conflict resolving process
  Unknown priority rules

## Slide 4: Regulation and Status of ASM Organization
Regulation in place
  ICAO, EU, national
ASM organization (by the book)
Concerns
  ASM 1
    Area establishment process was not suitable for user demands
  ASM 2
    AMC – civil-military coordination (mainly for commercial traffic and military areas)
    CIV AA – AD-HOC approval by an ANSP via NOTAM for 3 months (SR – SS)
    Pre-tactical approval process completely avoided (D-1) – conflicts on the day of activity
  ASM 3
    Tactical approval on the day of activity – increased workload for ATCOs, restrictions in approval or rejected requests
    Actual status for planning purposes – unknown (ask a relevant ATC unit)
HLAPB
(ASM 1)
CIV AA
AMC
MIL AA

## Slide 5: Assessment of Lower Airspace
Continuous growth of users demands
Uncontrolled "G" class of airspace limited to 1000 ft AGL
Published areas
  Non AMC-manageable military areas (P, R & D)
  Limited to small enclaves in the vicinity of airfields
  Non-adequate for user needs
Process of establishing a new area
  Duration of the establishment process
  Pressure on the organization and ASM system (continuous impact & safety assessments)
  Growth of requests for new AD-HOC areas on a daily basis
Gap in the regulation
  Users avoiding the full establishment process for new areas
  Continuous renewal of the approval for AD-HOC-created areas (permanent areas)
Procedures on a daily basis
  Non-manageable areas
  General announcement by NOTAM (SR – SS)
  For actual activity? (contact the relevant ATC unit)
Safety concerns
  Pre-flight briefing (someone may be there)
  Actual usage and efficiency (unknown)
  Education of users (workshops, panels, forums, etc.)
ASM tools and information dissemination
  Information dissemination by NOTAMs (too many with a general time of activation)
  Communication with the relevant ATC (by phone)
  General approval (by fax or e-mail / on paper)

## Slide 6: Preconditions for Implementation
ASM implementation at 3 levels
  Civil-military coordination
  CDM process established
Implementation and adjustment of the regulation
  ICAO, EU and national
  Priority rules
Airspace demand analyses
  Actual user needs
  Assessment of existing areas
  Actual usage of existing areas and airspace
Existing procedures
  LoAs
  Procedures for fast CDM and booking processes
Safety concerns
Existing tools and means of communication
  Real-time information about the actual airspace status
  "Online" communication between the user and ASM
  Enhanced planning process
MODULAR, FLEXIBLE ENVIRONMENT
ASM ORGANIZATION &
PROCEDURES
ASM TOOLS

## Slide 7: New Deal with Users
Modular flexible structures – proposal
Defined net of modular flexible structures (segmented airspace)
Conducted Safety Assessment of segmented airspace and structures
Determined priority rules
AMC as a focal point at ASM 2 and ASM 3 levels
  Responsible for management on a daily basis
  Coordination between stakeholders
Implemented fast CDM process
  Booking, activation and release procedures according to the FUA principles through ASM 2 and 3
  Easily accessible ASM tool supporting the CDM process
Net of structures published in AIP and the ASM tool (AMC Portal)
  Available to registered users according to the priority rules
CDM
USERS
AA, AMC
FMP
ATC
CDM
USERS
CESUP,
AMC
FMP
ATC
D-1 reservation
D tactical approval
ASM TOOL
Priority rules

## Slide 8: Implementation Process
Changing the types of military areas
  From non AMC-manageable P, R, D areas to the AMC-manageable TRA and TSA areas
Canceling all present civil areas for sporting activities
  In respective airspace where new fragmented, modular, flexible structures are to be applied
Setting up a net of new fragmented, modular, flexible structures
  Suitable for use by all users (civil or military)
  Net of D-AMA, TRA and TSA AMC-manageable areas
  Publication in the respective AIP and given to the AMC for day-to-day management
Regulatory framework adoption
  To enable new procedures and supporting tools to be implemented
  Implementation of new procedures through ASM tools in order to strengthen the execution of the new concept
Trial phase of the project
  Measurement of key performance indicators
  Implementation reassessment and the implementation of lessons learned
Operational use of new flexible, modular, fragmented areas on a daily basis
  Continuous measurement of key performance indicators

## Slide 9: Design Methodology
Lateral fragmentation of airspace
  Small areas (GND − 9500 ft)
  Lateral boundaries designed on the known-landmark principles (VFR activities)
New net of areas
  Suitable and available for various users and types of activities
3 possible area statuses (D-AMA, TRA, TSA)
  based on the type of activity or minimum equipment requirement
Fast and efficient CDM process
  Simple booking process
  Defined rules of use, avoidance, transit (where applicable) and minimum equipment requirements

## Slide 10: Purpose of Areas
D AMA
Applicable to all civil users who fly by the "see and avoid" principle
Class "G" airspace
Crossing of VFR traffic allowed with info about entering the "G" class airspace
TRA
Applicable to civil and military users equipped for the RMZ, TMZ
Airspace retains the class of airspace from which it is temporary segregated
Crossing of IFR possible after previous coordination
Crossing of VFR possible after previous coordination and if equipped with a transponder
TSA
Applicable to all users (mainly state users) who need a segregated area exclusively
Area manager is responsible for the safety within the area
Crossing is not allowed

## Slide 11: Gains of Modular Flexible Structures
FUA/AFUA implementation in lower airspace
  More airspace available for users
  Real-time information about segregations in airspace
  Overview of the actual and planned situation in airspace
  Overview of airspace available for booking (volume and time)
Simple and fast booking process (D-7 to D-1)
Realistic time of activation
Fast airspace release process after activity is completed
"Online" communication between users and the ASM through an ASM tool
Favorable ratio of the published and AD-HOC structures

## Slide 12: Post-implementation Analysis
New areas are used everyday
  Vicinity of airfields – maximum use
  Connected structures for bigger events
  Overflights between airfields and cooperation between users
  Significant rise of sporting activities
  Fast and safe segregation for military and police operations on demand
More efficient planning process
  Planned/used
  D-AMA areas ("class G") – mostly used
Simplicity of the process
Safety of all airspace users
CDM − Requested/approved/used
Chart: 
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
TIME REQUESTED | 4.1958 | 2.6667 | 0 | 16.6604 | 48.5972 | 61.5382 | 100.1667 | 263.6632 | 119.5069 | 90.4167 | 23.7847 | 11.5972
TIME PLANNED | 4.1958 | 2.6667 | 0 | 16.6465 | 47.8542 | 61.9132 | 100.6458 | 274.5347 | 130.4132 | 93.566 | 22.6111 | 11.7535
TIME ALLOCATED
TIME UPDATE ALLOCATED
TIME ALLOCATED (CHANGED AND UPDATED)
TIME USED
TIME ACTUALY USED (UNTIL CANCELLED) | 2.2917 | 0 | 0 | 10.8194 | 24.434 | 25.3264 | 47.7187 | 164.5347 | 52.0868 | 23.0764 | 7.4063 | 3.9583
Chart: 
| JUL | AUG | SEP
TIME REQUESTED | 100.1667 | 263.6632 | 119.5069
TIME PLANNED | 100.6458 | 274.5347 | 130.4132
TIME ALLOCATED
TIME UPDATE ALLOCATED
TIME ALLOCATED (CHANGED AND UPDATED)
TIME USED
TIME ACTUALY USED (UNTIL CANCELLED) | 47.7187 | 164.5347 | 52.0868

## Slide 13: AMC Portal – Web Tool
Internet is a huge part of our life; why not use it for the benefit of all users on a daily basis
AMC PORTAL – current status
All information in one place, for everybody to see and use

## Slide 14: Conclusion
FUA/AFUA implemented in entire airspace
Planning is realistic with a fast release process when there is no further need for segregation
Improved safety of all users
Airspace user
Available airspace for all kinds of activities based on the actual needs (D-AMA, TRA, TSA)
Increase in potentially segregated airspace in practice means an opportunity for greater airspace efficiency at allocation

## Slide 15
Q&A?
  Thank you for your attention!